## Slide 1: Direct connect Diagram
5V
GND
A0
20=SDA
21=SCL
10 = PWM for Servo
9 = PWM IN1 (evk)
8 = PWM IN2 (evk) 7 = left limit (H = hit, L = not hit)
6 = right limit (H = hit, L = not hit) *7,6 (pulled up to 5V by Arduino)
5 = ball in cup (H = in cup)
No laptop,
Need VCC: 9-12V
Laptop
24V
5V
5V
Vref has onboard divider
IN2 IN1
BD63150FM EVK
Right
Left
(**)Connect motor to EVK for correct left-right joystick = left-right cup
**
5V

## Slide 2: ProtoShield connect Diagram
Pin-10 (Servo) | 5V | ND | x
Pin-9 (PWM1) | 5V | GND | x
Pin-8 PWM2 | 5V | GND | x
x | 5V | GND | Pin-7 (Left Limit)
x | 5V | GND | Pin-6 (Right Limit)
Pin-5 (opto) | 5V | GND | x
 | 5V | GND | A0 (Joystick)
SCL (lcd) | 5V | GND | SDA (lcd)

## Slide 3: About “dip switches”
These dip switches are to “simulate” the limit switches.
Position:
Down = pin-6 or pin-7 is grounded (ie. Limit is simulated engaged)
Up = pin-6 or pin-7 is floating (when connected to actual jig, the dip switches should be in “up” position
L-LIM
R-LIM
UP
DOWN